## Slide 1: Chapter 10 Design for Maintainability
Maintenance Requirements
Design Methods
Human Factors & Ergonomics
I fix things!
Notes: Those maintainability issues that are influenced by the product’s design need to be addressed early in the design phase. This chapter highlights several such design considerations.

## Slide 2: Maintainability
Specify Maintainability
Goals and Concepts
Allocate Maintainability
to Components
Implement Design
Methods
Address Secondary
Factors
goals
achieved
?
System Effectiveness
Life Cycle Costs
no
Complete
Design
Maintenance Analysis
Prediction & Assessment
yes
Notes: Similar to the reliability design process, is the maintainability design process. Maintainability goals and specifications are determined based upon system effectiveness requirements and life cycle cost considerations. The system maintainability goals must be allocated to the components composing the system. Using design methods such as fault isolation techniques, modularization, and accessibility considerations, these component goals may be realized. Secondary factors that impact upon maintainability include spare parts levels and the level of the maintenance resources such repair persons, tools, and test equipment. Through maintainability demonstrations, the achievement of the goals can be assessed. If they have not been met, then further design is necessary.

## Slide 3: Measurements and Specifications
Mean time to repair (MTTR)
Median time to repair (other quartiles)
Max time tp where Pr{T<= tp} = H(tp) <= p
Mean system downtime
Mean time to restore (MTR)
Maintenance hours per operating hr (MH/OH)
Notes: Based upon the repair time distribution that was presented in the previous chapter, several measures of maintainability are in use particularly as design specifications or goals. The six shown are the most common. The MTTR and median time to repair are measures of the inherent maintainability of the product. Specifying a maximum repair time, tp, that must be met with a specified frequency, p, based upon the repair time distribution is an alternate measure of the inherent maintainability. An example of this type of specification would be that 90 percent of the failures must be repaired within 8 hours.

## Slide 4: Mean System Downtime
Tp = the (mean) time between PM’s,
td = the system design or (economic) life,
MPMT = the mean PM time, and
m(td) = is the expected number of failures in the interval (0, td )
Notes: Mean system downtime is a weighted average of the unscheduled downtime and the preventive maintenance downtime. The weights are the relative frequency of performing each. This measure of maintainability would be important if PM was a significant requirement.

## Slide 5: Mean Time to Restore (MTR)
Notes: The mean time to restore includes the mean system downtime but also includes the mean delay time waiting for maintenance resources and the mean supply delay time waiting for spare parts. This measure of maintainability is useful if resourcing the repair process was part of the requirement.

## Slide 6: Maintenance Hours per Operating Hour (MH/OH)
MH / OH = (m(t) x MTTR x CREW ) / t
Or if preventive maintenance (PM) is to be included:
MH / OH
= [ m(t) x MTTR x CREW
+ (t / tp) x MPMT x CREWp ] / t
where CREWp is the average crew size for PM
Notes: Maintenance hours per operating hour may include both unscheduled and scheduled hours. This measure takes into account not only the failure rate, PM frequency, and repair time but also the crew size. It is a measure of the workload and not the downtime. This measure can be multiplied by an average maintenance labor rate to convert to maintenance cost (dollars) per operating hour. To the degree that the skill levels required to perform the maintenance are reflected in the average labor rate, this measure would allow comparisons among products requiring different levels of skill, experience, or training.

## Slide 7: Maintenance Concepts & Procedures
Repair versus discard and replace
the PM schedule and associated tasks
For repairable units, for each failure mode, the level of repair (e.g. local, service center, or factory) ,
For each repair task, the required skill levels, tools, test equipment, and technical manuals ,
The number of repair channels and spare parts
Notes: As part of a maintainability design plan, maintenance concepts and procedures such as those listed must be determined.

## Slide 8: Level of Repair
Factory
Centralized Repair Facility (Depot)
Local Repair
On-site Repair
increased specialization
special tools and test equipment
economy of scale
decreased response time
routine maintenance
reduced skill levels
Notes: There are trade-offs between the level of repair and response times, skill levels, resources, and type of maintenance that can be performed.

## Slide 9: Maintainability Design Features
Maintainability
Reliability
Fault
Isolation
Modularization
Repair
vs
Discard
Standardization
Interchangeability
Level of
Repair
Diagnostics
Spares
Levels
Repair
Resources
Skill Levels
Training
Tools
Maintenance
Organization
Facilities
Test
Equipment
Human
Factors
Life
Cycle
Cost
Accessibility
PM
Notes: Maintainability factors can be considered to be primary (inherent) or secondary depending upon whether they are part of the inherent product design or not.

## Slide 10: A Simple Cost Model
td = design or economic life in operating hours,
Ca = acquisition cost
Cf = fixed cost of a failure (e.g. spare parts)
Cv = variable cost per hour of downtime
(e.g. labor rate x crew size, loss of production, etc.)
Then Cost = Ca + (td / MTBF ) (Cf + Cv MTTR)
assumes a renewal process
Notes: Presented here is a simple cost model that can be used to compare two or more designs. Both the reliability (MTBF) and maintainability (MTTR) impact upon the computed cost.

## Slide 11: Exercise
A voltage regulator may be obtained from two vendors. Vendor A’s
regulator costs $150 and Vendor B’s regulator costs $200. Vendor A’s
is less reliable with a MTTF of 1800 days while Vendor B’s MTTF is 2600
days. Vendor A’s regulator has a more modular design and is therefore
easier to replace with a MTTR of 4 hr while Vendor B’s regulator takes
6 hr. to replace. If a failed regulator must be replaced at its unit cost,
which product should be used? The labor rate is $45 per hour and the
design life of the regulator is considered to be 10 yr.
Vendor A
Vendor B
Notes: Apply the cost model to this example. Work this problem before viewing the solution on the next slide.

## Slide 12: Exercise - solution
Vendor A: 150 + (10 x 365 / 1800) [150 + 45 (4) ] = $ 819
Vendor B: 200 + (10 x 365 / 2600) [200 + 45 (6) ] = $ 860
Notes: The solution! I bet you got it right, didn’t you?

## Slide 13: Component Maintainability
MTTRs= system maintainability goal
fi = expected number of failures of ith component
qi = number of identical units of component I
n = number of components
Set MTTRs and use trial and error and iteration to find MTTRi
Notes: Equation 9.23 can be worked in reserve to allocate product or system maintainability to its components. Another approach is to use trial and error to vary component MTTRs until the system MTTR is obtained.

## Slide 14: Design methods
Fault Isolation and self-diagnostics
Parts Standardization and Interchangeability
Modularization and Accessibility
Repair vs. Replace
Proactive Maintenance
Notes: Once component maintainability goals have been determined, these goals must be achieved through proper product design. Listed are common design initiatives that have direct impact upon all of the maintainability measurements.

## Slide 15: Design Methods
access
diagnosis
replace or repair
verify
& align
Accessibility
fault
isolation
modularization
parts standardization
interchangeability
repair vs discard
human factors
supply
delay
maintenance
delay
maintenance and
spares provisioning
increase
tolerances
Notes: The activities that occur during a product’s downtime provide insight into several of the design initiatives. The objective is to reduce total downtime. Each activity has one or more corresponding design initiatives that can reduce its completion time.

## Slide 16: Fault Isolation
Manual
  trial and error process
  may use test equipment such as oscilloscopes, gauges, meters, etc.
  process of elimination
Automatic
  failed unit is removed and connected to computerized test station or test set is transported to system and connected
  computer executes one or more diagnostic programs
Self-diagnostic
  built-in test equipment (BITE)
  upon failure, system switches to diagnostic mode
  must detect and then isolate the fault
high
skill
low
skill
Notes: Fault isolation or trouble-shooting is often the most time consuming repair activity. It often requires the highest skill levels, training, and experience. Therefore, by including fault diagnostics in the design of the product, considerable improvement in maintainability may be realized.

## Slide 17: Fault Isolation - test equipment
System
test station
MTTRsys
R(t)
MTTRtest sta
Let T = avg time on test station
included
MTR = MTTRsys + [1 - R(T)] MTTRtest sta
Animated
Notes: When additional hardware (and software) is added for fault isolation, the reliability and maintainability of the fault isolation equipment can impact upon the system maintainability.

## Slide 18: Fault Isolation
Provide easy access to failed units
Clearly identify and group test points
A B C
D E F
G H I
Good design
Poor design
1
2
3
4
5
6
1
2
3
amps
volts
ohms
Notes: When using external fault isolation equipment, design connections for easy access and use.

## Slide 19: Parts Standardization
Reduce to a minimum the range (breadth) of parts which must be maintained and stocked.
Reduces training and skill requirements.
Simplifies coding and labeling.
Allows for fewer tools, test equipment, and tech manuals.
Improved part reliability will have an effect wherever the part is used.
Notes: Standardization of parts across product models (and even brands) can have a significant impact on maintainability.

## Slide 20: Interchangeability
A design policy that allows specified parts to be substituted
within an assembly for any like part.
Requires both functional and physical substitution.
Physical substitution requires standardization in mountings,
pins, connectors, etc. as well as compatibility in size and
required space.
Converse to interchangeability: If two components are not
intended to be functionally interchangeable, they should
not be physically interchangeable.
Notes: Interchangeability is an alternative to parts standardization. Parts that are not interchangeable ideally should not be compatible physically.

## Slide 21: Modularization
Isolates problem to a physical unit (module)
Supports remove and replace maintenance concept
Permits packaging against environment
  increases reliability
Minimize number of connectors
Reliability of all components in a module should be equal
Notes: A module can be defined as an assembly that can be removed and replaced. Modules often are not repaired. Modules should be designed for easy access and removal.

## Slide 22: Accessibility
Design accessibility down to the discard level.
High failure components should be more accessible than those that seldom or never fail.
Size, weight, and clearances must be considered in designing removal modules.
Ideally removing a failed unit should not require removal of a unit that has not failed.
Notes: Accessibility to failed components is a critical maintenance design consideration.

## Slide 23: Accessibility
Direct access
Opening with no cover
Pull out drawers
Hinged door access
Removable panels
  quick open captive fasteners
  non-captive fasteners
  screws or bolts
  rivets
Remove other components
most preferred
least preferred
Notes: A hierarchy of accessibility design features.

## Slide 24: Accessibility
good
bad
most preferred
least preferred
No tools needed
Grip head allows
use of wrench
must be drilled
out if slot is
damaged
Notes: A hierarchy of fasteners exists as well.

## Slide 25: Accessibility
9.8”
Notes: Accessibility includes sufficient work space.

## Slide 26: Modularization & Connectors
good
design
poor
design
1
2
module
Notes: Minimize the number of connections required among modules.

## Slide 27: Modularization & Connectors
(color) code connector and receptacles
Remember, however, that 5% of population is color blind!
Notes: Color code and clearly mark connectors and receptacles.

## Slide 28: Modularization & Packaging
plug-in
plug in + connectors
fastening (screws, bolts, etc.)
fastening + attaching leads
plug-in + soldering contacts
fastening + soldering contacts
most preferred
least preferred
Notes: Another hierarchy. Plug and play is an important maintainability concept here.

## Slide 29: Good Maintenance Design Methods?
Fault Isolation
(failure mode codes
and location indicators)
Accessibility
(pull out drawers)
modularization
supports operator maintenance
Notes: Today’s reproducing machines typically incorporate good maintainability design features.

## Slide 30: Poor Maintenance Design Methods?
special tool
to replace failed
headlamp
nonstandard
parts
accessibility?
modularized
discard and replace
live-softly
fault isolation
broke
Notes: Today’s automobiles do not always incorporate good maintainability design features.

## Slide 31: Repair vs. Replacement
f = the number of part failures over the life of the system,
c = unit cost of the part,
ar = fixed cost of repair
ad = fixed cost of discarding where ad < ar
br = cost to repair a failure (e.g. labor rate x crew size x MTTR),
bd = cost to remove and replace a part where bd < br ,
k = condemnation fraction
A Cost Trade-off Model
repair cost = ar + br f + c k f
discard cost = ad + (c + bd ) f
Notes: A maintainability design question is whether to replace or repair a failed module. This simple cost model allows for comparison of these two alternatives as a function of the number of expected failures over the life of the module.

## Slide 32: Repair vs. Replacement
ad + (c + bd ) f <= ar + br f + c k f
If
Then discard
c
f
discard
repair
br-bd
1-k
Notes: If the intersection of the number of expected number of failures and the unit cost of the module falls above the plotted curve, then repair the module; otherwise replace (discard) it.

## Slide 33: Example - circuit board
ar = $ 20,000 (primarily test equipment and facilities) ,
ad = $ 1200 (warehouse overhead for the spares),
br = $ 768 / failure ($48 / hr labor x 8 hr MTTR x 2 crew members),
bd = $ 24 / failure ( $48 / hr labor x .5 hr R&R x 1 crew member),
k = .05
c = 783.2 + 19789.5 / f .
Notes: An example from the text. I bet you could construct an Excel spreadsheet to do these calculations and plot the curve? Go ahead, try it!

## Slide 34: Replacement Model
Cu = unit cost,
Co = operating cost per unit of time,
Cf = cost of a failure
t = replacement time
Notes: Components that are initially cost effective to repair may eventually begin to wear out and demonstrate increasing failure rates. At some point in time, it may no longer be economical to continue to repair them. This model assumes minimal repair with an increasing intensity function during the life of the component. The objective is find a replacement time, t*, that minimizes the sum of the unit cost, operating cost, and failure cost per unit of time.

## Slide 35: Replacement Model
For the power law process:
what if b <= 1?
Notes: For the power law process intensity function, the solution shown is obtained. What is the problem when b <= 1?

## Slide 36: Example 10.6
A repairable machine has a NHPP with an intensity function
of (t) = 2 x 10-6 t with t measured in operating hours. If the
cost of a failure (repair) is $500 and the unit cost is $21000,
then t* = (21000/[(500)(10-6 )].5 = 6481 operating hours.
Replace at 6481 hr
Notes: An example from the text.

## Slide 37: Preventive Maintenance
Cr = cost of a repair or replacement action,
Cs = cost of a preventive maintenance activity, where Cr > Cs ,
T = time in hours between preventive maintenance activities, and
(t) = intensity function of a NHPP
Expected hourly cost of unscheduled maintenance:
Notes: A model that is similar mathematically to the replacement model is the above preventive maintenance model. The assumption is that PM restores the system to “as good as new.” Therefore only the expected number of failures from time 0 to T (the PM interval) is found. The cost trade-off here is between the cost of failures (unscheduled maintenance) and the cost of performing a PM (scheduled maintenance).

## Slide 38: Preventive Maintenance
Total expected hourly cost:
For power law process:
Notes: Minimizing the total cost per unit of time under the power law failure process results in the solution shown.

## Slide 39: PM - Example
A grinding machine has a power law process (NHPP)
with b = 2.4 and a = 2.55 x 10-5 hours. The cost of
scheduled maintenance is $20, and the cost
of an unscheduled repair is $80. Find the least cost
preventive maintenance interval.
Notes: The example from the text. Create your own example and solve it.

## Slide 40: Human Factors
Anthropometry - study of human body dimensions
Biomechanics - how movements are performed
Physiology - study of human processes such as muscle movements and joint system
Psychophysics- study of human perceptual capability
Perception - how information is received, stored, and interpreted
Human Performance - how humans interface in the workplace
Brain
Cerebellum
Cranial nerves
Cervical nerves
Spinal cord
Thoracic nerves
Lumbar nerves
Radial nerve
Median nerve
Ulnar nerve
Sacral nerves
Sciatic nerve
Tibial nerve
Esophagus
Lungs
Heart
Liver
Pancreas
Large intestine
Small intestine
Bladder
Stomach
NERVOUS SYSTEM
Notes: Maintenance is large a human activity. Therefore when designing for maintainability, the capabilities and limitations of the typical repair person must be addressed. This leads us to the study of human factors which includes the six topic areas shown.

## Slide 41: Design for Maintainability
Controls
Displays
Tool and equipment design
the workplace
the environment
Human Factors Considerations:
The Coffee is terrible.
I can’t work here!
Notes: Human factors impacts on both the product design and the environment for repairing a failed product.

## Slide 42: Controls and Displays
digital
analog
Displays should be
placed at eye level!
Notes: Consider during the design of controls and displays, how the maintainer will interface with them.

## Slide 43: Selected Human Factors Data
Notes: Published human factors data can be used to design equipment that is easily maintained by 95 percent of the population.

## Slide 44: The Working Environment
Noise
  pain at 130 db
Illumination
  50 foot-candles for dials, gauges, and meters
Vibration
  exposure limits depends on frequency and amplitude
Ambient Air
  temperature (550 to 750 F.)
  humidity
Notes: A happy and comfortable maintainer is a good maintainer!

## Slide 45: Human Reliability
human reliability: Rh = 1 - e/n
n = number of tasks
e = number of unsuccessful completions
Task error rate (per task)
read 5 letter word incorrectly .0003
read digital display wrongly .001
leave light on .003
select wrong switch among similar .005
read 10 digit number incorrectly .006
mate a connector wrongly .01
wrong selection -vending machine .02
dial 10 digits incorrectly .06
fail to check hardware unless specified .1
fail to notice wrong position of valves .5
Notes: Human error should be considered when designing for maintainability. Remember, what can go wrong, will, at some point, go wrong.

## Slide 46: Human Errors
random - unbiased
  stress level too high -panic, time constraints
  stress level too low - boredom
systematic
  biased, casual effect
  improper tools
  incorrect procedures
sporadic
  carelessness
  forgetfulness
Notes: Human errors can be categorized as random (chance event), systematic (occurring frequently and repeatedly), or sporadic (occurring occasionally).

## Slide 47: Causes of Human Error
Poor training and low skill levels
Inadequate maintenance or operating procedures
Inadequate supervision
Poor working environment
Improper or lack of motivation
Notes: Can you add to this list from your own experiences?

## Slide 48: Skill Levels
Effective maintainability is dependent upon the designer’s being fully aware of the limitations of maintenance personnel.
The average technician performing maintenance should not be expected to:
  read at higher than ninth grade level,
  perform any mathematical calculations including simple addition and subtraction,
  consolidate or integrate any information from several different sources,
  collect, process, or report any unusual or complex data,
  and post data from one form to another or keep any records.
Maintainability Engineering, US Army Materiel Command, 1965
Notes: This organization had a low expectation of the ability of its maintainers.

## Slide 49: Human Factors Considerations
minimize skill requirements
minimize tools and test equipment
minimize adjustments and calibrations
allow for visual inspection if possible
put handles on heavy equipment
use bad-good or redline meters - avoid numerical readouts
Notes: This is the ideal situation from the human factors side. What about costs?

## Slide 50: In Conclusion Ideal Design Criteria for Maintainability
Maintenance is available on site with no waiting
Fault isolate is immediate and accurate
Access is direct
Necessary spare parts are on-hand
Maintenance is remove and replace with no tools required
No requirement to recalibrate, adjust, align or otherwise verify
Notes: Are all of your products designed for maintainability?