## Slide 1: Chapter 18 Implementation
Objectives, Functions, and Processes
The Economics of Reliability
Data Collection Systems
Mom, what do reliability engineers really do?

## Slide 2: Reliability Engineering Objectives, Functions, and Processes
The overall objective of reliability engineering is to insure that the final product will be both economically reliable and reliably safe.
Economically reliable means that the product’s observed reliability has been established with consideration of the life cycle costs involved.
  This would include both the acquisition costs and the costs of failures (including perhaps customer goodwill costs).
Reliably safe requires designing sufficient reliability into the product to insure that the probability of accidents, injury, or death resulting from a product failure is within an acceptable limit.

## Slide 3
Quantifying reliability requirements as design goals or specifications,
Allocating or apportioning reliability requirements to system components and parts,
Applying reliability design methods during product development (parts selection, derating, etc.),
Performing R&M analysis (block diagrams, stress-strength, redundancy, R&M trade-offs , etc.).
Conducting a FMEA program,
Participating in design reviews,
Establishing test procedures and conducting reliability testing,
Performing a reliability prediction or demonstration,
Developing a reliability plan.
Can you list the functions of a reliability engineer for us?

## Slide 4: Maintainability Engineers
The objective of maintainability engineering is to insure restoration of a failed system or product is accomplished in a timely and safe manner.
The economics of repair considers the trade-offs among product reliability, repair time, maintenance resources and spare parts requirements.
With these grades, I can be a maintainability engineer.

## Slide 5
Quantifying maintainability requirements as design goals or specifications,
Allocating or apportioning maintainability to system assemblies and components,
Applying maintainability design methods during product development (fault isolation, modularization, etc.)
Performing maintainability and availability analysis (R&M trade-offs , maintenance resourcing, establishing preventive maintenance intervals, spares provisioning, etc.).
Participating in design reviews,
Performing a maintainability prediction and demonstration,
Developing a maintainability plan.
Grandpa, can you tell me the story again about your days as a maintainability engineer when you maximized profits through maintainability design reviews?

## Slide 6: The Economics of Reliability

## Slide 7: Cost versus Availability

## Slide 8: System Repair Cycle

## Slide 9: Product Life Cycle Activities
Product Phase | Sources of R&M Data | R&M Tasks
Initial design | Databases (Mil-Hdbk) Vendor specifications Comparability Analysis | Establish goals & specs R&M allocation life cycle costing FMEA
Detailed design & prototyping | Reliability & product testing Maintainability demonstration reliability growth testing | R&M predictions Design methods and trade-offs FMEA
Production | Quality Control Burn-in and stress testing Acceptance inspections Life testing | Redesign and modifications
Operations | Field Data Warranty data | Preventive maintenance Overhaul Sparing & parts replacement

## Slide 10
Data Element Definition
Failure Number A sequential number identifying a failure record
Date/Time Date and time the failure is recorded
Part ID The specific component or part which has failed
Failure Time The age of the part (in a reliability sense) at the time of failure (not when discovered) measured in failure time units (e.g. operating hours, cycles, miles, etc.).
Failure Mode The exact nature of the failure (short, overload, impact fracture, power failure, break, etc.)
Failure Cause If identifiable such as excessive vibration, fatigue, corrosion, power surge, human error, or Mechanism maintenance induced, normal fatigue wear, etc.
What data should I be collecting?

## Slide 11: More R&M Data Elements
Data Element Definition
Start Repair The date/time hands-on corrective maintenance began (does not include time waiting for spares or maintenance resources)
Stop Repair The date/time all restoration has been completed
Action Taken The type of maintenance performed to correct the failure such as remove and replace, minor adjustment, calibration, rebuild, etc.
Crew Size The number of individuals performing corrective maintenance (if the number varies during restoration then use a weighted average)

## Slide 12: Service Contracts
Example 18.2
Statistics show that 7 percent of all VCRs sold need servicing during their first year and 43 percent need servicing within five years. If Weibull failure times are assumed, the parameters can be estimated by solving the following two nonlinear equations:

## Slide 13: Service Contracts
=1.272
= 7.86
MTTF = 7.292 yrs, tmed = 5.892 yrs., tmode = 2.338 yrs.
Std. dev. = 5.774 yrs., 90 percent design life = 1.34 yrs
R(4 yrs) = .65, R(10) = .26

## Slide 14: Service Contracts
=1.272
= 7.86
The average cost of a repair is $95.00. The first year is
covered by the warranty. The customer can purchase a
Service contract for the second year at a cost of $50.
The economics; the expected repair cost the second year:

## Slide 15: 18.6 Software Reliability
The probability of failure-free operation of a computer program for a specified time in a specified environment.

## Slide 16: Software Reliability
Concerned with how well the software functions to meet the requirements of the customer.
Redundancy in the hardware sense does not work.
Represents a user-view of software quality.
  relates to operation rather than design and testing.
Source of failures are faults
  originating from errors in requirements, design, coding
Changes continuously during (reliability growth) testing.
The user discovers a “failure”

## Slide 17: Fault (Defect) vs. Failure
Failures are dynamic occurring over time. Time (“age”) may be
measured as execution time, test time (labor hours or test execution hours), or calendar or elapsed time.
Software reliability can be measured by
1. time of failure
2. time between failures
3. cumulative failures at time t
4. total failures in a time interval
Alternate approach is to define reliability as the probability that the software will fulfill its mission. For example, two distinct modules S1 and S2 perform the same identical function where time to execute T1 < T2. If both modules generate incorrect output, which is more reliable?

## Slide 18: Why treat failures as random?
Two sources of randomness:
The commission of errors by programmers, and hence the generation of faults, is a very complex, unpredictable process.
  therefore the location of faults within a program are unknown.
The conditions of execution of a program are generally unpredictable.
  therefore the paths to be taken cannot be determined.
A fault is a defect (bug) in a program which causes a failure.
A fault is a property of a program rather than a property of its execution.

## Slide 19: Failure Distribution affected by:
The number of faults in the software
  number introduced - number removed
  introduced during coding but may be a result of requirements or design defects
The execution or operational profile of the system
  cannot remove a fault unless detected
  detection resulting from execution depends on the length of execution time and the operating environment
Faults may be found through inspection (code audits), compiler diagnostics, design and code reviews.

## Slide 20: Cascading Errors
Requirement
Specification error
High level
design error
Generates high
level design
error
Generates coding
error
Generates low
level design
error
Generates low
level design
error
Generates coding
error
Low level
design error
Generates coding
error
Coding
error
As a software engineer,
I know how important
it is to find errors early
in the development
cycle.

## Slide 21: Software Reliability Models
Definition:
A Mathematical model constructed for the purpose
of assessing the reliability of software from specified
parameters which are either assumed or are estimated
from observable data.
Primary functions:
R(t) - reliability at time
(t) - intensity function
n(t) - expected (cumulative) number of failures at time t

## Slide 22: Software Reliability Models
Time-to-failure models
  characterized by a time to next failure distribution
  typically based upon the exponential
Error counting models
  characterized by the number of remaining errors
  typically based upon the Poisson
Unique Models
  error complexity model

## Slide 23: Reliability Models - typical assumptions
Monotonic (decreasing) failure intensity function
Faults are independent
Perfect and instant removal of faults once discovered (as opposed to batch fixes)
(Usually) a finite number of faults are present
Time between failures are independent
Intensity function is related to number of errors remaining
NHPP (CFR between defect removals)

## Slide 24: The Reliability Engineer
Reliability Engineers are a sad and embittered race. A lonely group despised by both the design team and management; their sole function being to generate failures. And generate failures they will! For it is their very life, their ambrosia, their reason for being. Many a good designer has quietly disappeared after receiving one too many failures. Management has lost their stock options because the reliability growth curve did not grow. No wonder the poor reliability engineer dines alone, talks to no one, and has no friends. Their only hope to escape the despair of the day to day job comes with the knowledge that all things must fail, and eventually as the reliability life test runs to its inevitable conclusion, so will they.
I am going to be a reliability engineer.