## Slide 1: Chapter 18 Section 8.5 Fault Trees Analysis (FTA)
Don’t get caught out on a limb of your fault tree.

## Slide 2: Characteristics
Graphical design technique
Alternative to reliability block diagrams
Broader in scope
Perspective on faults rather than reliability
Model events rather than components
Faults include failures
Focus on a catastrophic event (top event)
Top-down deductive analysis

## Slide 3: The Four Steps to a FTA
(1) Define the system, its boundaries, and the top event,
(2) Construct the fault tree representing symbolically the system and its relevant events,
(3) Perform a qualitative evaluation by identifying those combinations of events which will cause the top event,
(4) Perform a quantitative evaluation by assigning failure probabilities or unavailabilities to the basic events and computing the probability of the top event.

## Slide 4: Fault Tree Symbols
AND gate - a logic gate where an output event occurs only when all
the input events have occurred.
OR gate - a logic gate where an output event occurs if at least one of
the input events have occurred.
Resultant event - a fault event resulting from the logical
combination of other fault events and usually an output to
a logic gate.
Basic event - an elementary event representing a basic fault
or component failure.
Incomplete event - an event that has not been fully developed
because of lack of knowledge or its unimportance.

## Slide 5: General Structure of a Fault Tree
Top Event
System Failure
Resultant Events
AND/OR gates
Basic
Events

## Slide 6: Example of AND / OR Gates
Tank Ruptures
OR
Overpressure
(a)
Overpressure
Excessive
Temperature
Relief
Valve
Fails
AND
(b)
Wall
Fatigue
Failure

## Slide 7: Example of AND / OR Gates
Excessive
Temperature
Relief
Valve
Fails
AND
Tank Ruptures
OR
Overpressure
(c)
Wall
Fatigue
Failure

## Slide 8: Alarm System Example
automatic
sensor
power
source
backup
power
alarm
switch
meter
observer

## Slide 9: Alarm System Fault Tree
T- Alarm Failure
A-Power Failure
G-Manual Alarm
Failure
E-Primary
power fails
F-Backup
fails
I-Human
Error
B-Sensor Failure
J-Switch
fails
K-Meter
Fails
H-Auto
Sensor
Fails
AND
AND
OR
OR
C-Alarm
Failure
D Secondary
alarm failure

## Slide 10: Boolean representation of Top Event

## Slide 11: Example

## Slide 12: Example Equivalent Fault Tree
T = A U E

## Slide 13: Minimal Cut Sets
A cut set is a collection of basic
events which will cause the top
event. A minimal cut set is one
with no unnecessary events. That
is, all the events within the cut set
must occur to cause the top event

## Slide 14: Example
2
E,F
G,H
C
D
1
A
B
C
D
3
E,F
I,H
J,H
K,H
C
D

## Slide 15: Example Cut Sets
1 2 3 4 5
A A A A A
B C, D E, D E, E E
F, D E, A
F, E
F, A

## Slide 16: Quantitative Analysis
P(T) = P( M1 U M2 U …U Mk )
= P(M1 ) + P(M2 ) + ... + P(Mk )
If not:
if independent
If cut sets are mutually exclusive:
If P(M) < 10-3
P(T) = P(M1) +P(M2) - P(M1) P(M2) + etc.
Then P(M1) P(M2) < 10-6

## Slide 17: Example

## Slide 18: Brake System Revisited

## Slide 19: One Last Example
Top Event
A
B
C
M
I
H
F
L
N
G
J
K
Q
P
OR
AND
E
D
OR
AND
OR
AND
OR
R
S
OR
T = A  B  C
= (D  E)  (H  I)  (L  M  N)
= [D  (F  G)  [H  (J  k)]
 [L  (P  Q)  N]
= [D  (F  G)  [H  (J  k)]
 [L  (R  S  Q)  N]
P(T)  P(D) [P(F) + P(G)] + P(H) + P(J)P(K) + P(L) [ P(R) + P(S) + P(Q)] P(N)

## Slide 20: The Cut Sets
Top Event
A
B
C
M
I
H
F
L
N
G
J
K
Q
P
OR
AND
E
D
OR
AND
OR
AND
OR
R
S
OR
#1
A
B
C
#2
D,E
H
I
L,M,N
#4
D,F
D,G
H
J,K
L,R,N
L,S,N
L,Q,N
#3
D,F
H
J,K
L,P,N
L,Q,N