## Slide 1: Chapter 8 Design for Reliability
8.1 Reliability Specification
8.2 Reliability Allocation
8.3 Design Methods
Notes: This chapter is somewhat of a departure from the previous development. The focus is not on the development and use of reliability models, but rather on concepts and techniques for analyzing and influencing reliability particularly during the design process.

## Slide 2: 8.1 Reliability Specification The Reliability Design Process
Notes: The reliability design process begins by identifying reliability specifications and goals. Ideally these are related to and influenced by product costs and performance. Generally some allocation method is then required to translate product reliability into component and part reliabilities. It is then the function of the design engineer to achieve these reliabilities through the choice of technology, materials and parts selection, redundancy, and other design methods. Achieved product reliability is determined through reliability testing and other failure analysis techniques such as a Failure Model and Effect Analysis (FMEA). If the specifications and goals have not been met, then the design process must continue.

## Slide 3: Reliability Activities & Product Life Cycle
Notes: Product reliability can be influenced throughout the product life cycle and not only during design.

## Slide 4: System Effectiveness
Notes: When relating reliability specifications and goals to product performance, other factors may also need to be addressed. For example, if the product can be restored upon failure, then maintainability as a design parameter along with reliability will determine the percent of time the product is available to perform its intended function. Operational readiness is the probability that the product will be available when initially required (recall R(0) = 1 from a reliability perspective). Design adequacy is the probability that the product will successfully perform its function given that it is operational. For example, a copying machine may be functioning as designed but may not be able to produce copies at the rate and quality required. Since all three components of system effectiveness are probabilities, then
system effectiveness = operational readiness x mission availability x design adequacy

## Slide 5: Life Cycle Cost Categories
Notes: If enough resources are committed to the design and development of a product, then high system effectiveness (e.g. reliability) can be achieved. However, the costs may be prohibitive. Meaningful trade-offs between performance (e.g. reliability) and cost can be found when using the product life cycle cost.

## Slide 6: Life Cycle Cost
LCC = Acquisition Costs +
Operations Costs +
Failure Cost +
Support Costs –
Net Salvage Value
Where
Net Salvage Value = Salvage Value – Disposal Cost
Notes: Life cycle costs that are influenced by reliability can be divided into the categories shown. Acquisition costs could include purchase costs, manufacturing costs, design and engineering cost, reliability testing costs, etc. Support costs may include maintenance and parts supply costs including preventive maintenance. Failure costs include the cost of repair as well as the cost of downtime or non-availability of the product. It may also include warranty costs.

## Slide 7: Discounting Monetary Values
constant annual inflation rate
annual return on investment rate
then for small values of and .
Let
F is a future amount at the end of year d,
A is an equal annual amount observed over d years.
Notes: The time value of money must be considered if the life of the product extends beyond a couple of years.

## Slide 8: Life Cycle Cost Revisited
unit acquisition cost
number of identical units to be procured
fixed cost of operating
Co = annual operating costs per unit
Fs = fixed support cost
Cs = annual support cost per unit
Cf = cost per failure
t0 = operating hours per year per unit
td = design life (in years).
S = unit salvage value (a neg. value is a disposal cost)
Notes: Here is a more comprehensive life cycle cost model. These models can take on different forms with varying levels of complexity. When performing reliability design analysis, the key is to include only those costs categories that are affected by the reliability. For example, if the operating cost of the product does not change as a result of improved reliability, then operating cost need not be included.

## Slide 9: Example 8.1
Two designs are being considered for a new product operating
throughout the year and having the following characteristics:
Design 1: Cu = 1200, .02 /yr
Design 2: Cu = 1300, .01 /yr
The design life of the product is 10 years. A failure results in a
replacement at the unit acquisition cost (i.e. Cu = Cf ).
Assuming an interest rate of 5 percent, PA(.05,10) = 7.7217
Design 1: 1200 [ 1 + P/A(.05,10) .02 ] = 1385.32
Design 2: 1300 [ 1 + P/A(.05,10) .01 ] = 1400.38
Notes: A simple example to compare two products based upon their relevant life cycle costs. Cu is the unit acquisition (procurement) cost. Both designs have constant failure rates.

## Slide 10: 8.2 Reliability Allocation
In general: h(R1(t), R2(t), ... , Rn(t))  R*(t)
where Ri(t) is the reliability at time t of the ith component,
and R*(t) is the system reliability goal at time t.
or g(MTTF1 , MTTF2 , ..., MTTFn )  MTTF*
For series related components:
Notes: There are any number of ways of allocating the product reliability down to the components and parts. Trial and error is one. Shown here is a conceptual model of the desired result. The reliability specification assigned to each component when achieved must result in the desired product specification. This specification could take the form of a reliability at a specified time or possibly the MTTF. The function g represents the reliability configuration (series and parallel relationships) of the system.

## Slide 11: Exponential Case
Notes: If all components are CFR, in series, and independent, then the above relationships must hold in order to meet product specifications.

## Slide 12: ARINC Method
Assume components are in series, are independent, and
have constant failure rates.
Notes: A simple method for finding values of the component failure rates that will provide the product goal, is to improve each component failure rate in proportion to their current relative values. Lambda-star is the desired product failure rate. Show why this works.

## Slide 13: AGREE Method
t = system operating time
R*(t) = system reliability goal at time t
n = number of components
ni = the number of modules within component i
N = total number of modules in system = ni
ti = the operating time of the ith component, ti <= t
i = the failure rate of the ith component
wi = the probability the system will fail given component i has failed
Allocating an equal share of the reliability to each module
results in component i’ s contribution to the system reliability
being
Notes: A more sophisticated approach allocates the product reliability to the components based upon the number of modules or parts contained in each component and the components conditional probability of generating a system failure given the component fails.

## Slide 14: AGREE Method
= 1 -
note that
Notes: By setting these two reliability expressions equal, the one unknown (lambda-sub-i) can be solved for. The expression on the left is the conditional probability of that component i causes the system to fail given it fails times the probability that it fails assuming a CFR. The expression on the right is one minus the reliability of the ith component with respect to a system failure assuming that each module or part is allocated the portion of the system reliability.

## Slide 15: AGREE Method - Example
Component Import Index (wi) Oper hrs (ti) Nbr of modules -ni
Receiver .8 1000 25
Antenna 1 1000 15
Transmitter .7 500 23
Power Supply 1 1000 70
The total module count is 133. If the system reliability goal is .99,
then the reliability to be allocated to the ith component is .99ni /133 .
Notes: At last – an example.

## Slide 16: AGREE Method - Example
Component Failure Rate MTTF Reliability System Rel
Receiver 2.362 x 10-6 423,369 .99764 .99811
Antenna 1.1335 x 10-6 882,227 .99887 .99887
Transmitter 4.9676 x 10-6 201,303 .99752 .99826
Power Supply 5.2896 x 10-6 189,048 .99472 .99472
System 1.3753 x 10-5 72,713 .98879 .99
From the above table, the probability
of a component failure is 1-.98879 while
the probability of a system failure is 1-.99.
Notes: The solution.

## Slide 17: Redundancy
R* = R1 x R’ x R4
R’ = 1 - (1 - R2 ) (1 - R3 ) = R2 + R3 - R2 R3
or R’ = 2 R - R2
with solution R = 1 - (1 - R’ ).5
starter
motor
chassis
Notes: The previous method assumed all modules were related to the system in series. If redundancy is present, the previous methods for allocating reliability can still be employed. However, it is necessary to first group the redundant components into a single component in series. Once the grouped reliability is determined using the previous methods, then the components within the group can be allocated reliabilities.

## Slide 18: 8.3 Design Methods
Parts and Material Selection
Derating
Stress-Strength Analysis
Complexity
Choice of Technology
Redundancy
Notes: There are several methods the design engineer can use to increase component reliability.

## Slide 19: Material Selection
Structure
atomic bonding
crystal structure
defect structure
microstructure
MATERIALS
SCIENCE
Material
Properties
yield strength
hardness
fatigue life
creep
MATERIALS
ENGINEERING
Manufacturing
Process
casting
machining (cutting)
joining
heat treatment
assembly
Service
Performance
Stresses
corrosion
temperature
radiation
vibration
MANUFACTURING
ENGINEERING
R(t)
Notes: The choice of materials to use in the manufacture of a component should be based upon performance, cost, manufacturability, and availability. The properties of the selected material will have a direct effect on its reliability.

## Slide 20: Design Methods Parts and Material Selection
Tensile Strength
Hardness
Impact Value
Fatigue Life
Creep
Property of Materials
Metals
Polymers
Ceramics
Composites
Notes: Several of the more important properties affecting reliability are shown.

## Slide 21: Material Selection
Notes: Each category of material has positive and negative properties. Which category to select may depend upon which stresses are most dominate in the product environment.

## Slide 22: Tensile strength
Tensile strength measures the force required to pull something such as rope, wire, or a structural beam to the point where it breaks.
  Specifically, the maximum amount of stress that it can be subjected to before failure
  Yield strength - The stress a material can withstand without permanent deformation.
  Ultimate strength - The maximum stress a material can withstand.
  Breaking strength - The stress coordinate on the stress-strain curve at the point of rupture.
Compressive strength is the capacity of a material to withstand axially directed pushing forces. When the limit of compressive strength is reached, materials are crushed. Concrete can be made to have high compressive strength.

## Slide 23: Parts and Material Selection Tensile Strength
strain (in/in)
stress
(lbs/in2)
ultimate strength
yield strength
X
breaking strength
slope = E
Hooke’s Law: Stress = E x Strain
modulus of elasticity (lbs/in2)
Notes: Yield strength is important for parts subject to tension or compression forces.

## Slide 24: Another Stress-Strain Curve

## Slide 25: Hardness
Brinell - Bhn (kg/mm2)
Rockwell - R
Vickers - Vhn
resistance of material
to the penetration of an
indenter - used in
analyzing service wear.
Notes: Hardness is another mechanical property that is measured using the Brinell, Rockwell, or Vickers scale.

## Slide 26: Fatigue
The progressive, localized, and permanent structural damage that occurs when a material is subjected to cyclic or fluctuating strains at nominal stresses that have maximum values less than the static yield strength of the material.
  The resulting stress may be below the ultimate tensile stress, or even the yield stress of the material, yet still cause catastrophic failure.
In high-cycle fatigue situations, materials performance is commonly characterized by an S-N curve. This is a graph of the magnitude of a cyclical stress (S) against the cycles to failure (N).

## Slide 27: Parts and Material Selection Fatigue Life
nbr of cycles - N
stress - S
(lbs/in2)
endurance
limit
steel
S-N Curve: N = c S-m where c, m > 0
Notes: Repeated stresses on a part can result in fatigue failure. These fatigues curves can be generated in a lab facility for different material.

## Slide 28: Creep
The tendency of a material to move or to deform permanently to relieve stresses.
Material deformation occurs as a result of long term exposure to levels of stress that are below the yield or ultimate strength of the material.
Creep is more severe in materials that are subjected to heat for long periods and near melting point.
The rate of damage is a function of the material properties and the exposure time, exposure temperature and the applied load (stress).

## Slide 29: Parts and Material Selection - Creep
strain
time
Failure
Failure
moderate temperature
high temperature
Notes: Creep is the gradual deformation of material usually under constant stress and at relatively high temperatures.

## Slide 30: Failure modes
gross yielding
buckling
creep
brittle fracture
Low cycle fatigue
high cycle fatigue
corrosion
wear
thermal fatigue
yield strength
compressive strength
creep rate
impact energy
ductility
fatigue properties
electrochemical potential
hardness
coefficient of expansion
Failure Mode
Material Property
Notes: Failure modes are an observed way in which a part has failed. Identifying the proper material property to counter a known failure mode is a design activity.

## Slide 31: Material Failure Mechanisms
Overstress Failures
brittle fracture
ductile fracture
yield
buckling
large elastic deformation
thermal breakdown
Wear-out Failures
corrosion
dendritic growth (electrolytic process)
interdiffusion
fatigue crack propagation
diffusion (molecular migration)
radiation
creep
adhesive wear
Notes: Failures can be generated because an abnormal stress level is encountered or because of gradual stress encountered over the life of the component.

## Slide 32: Derating
(applied voltage) / (rated voltage)
Notes: Derating is a design technique where a part is selected that has a higher stress rating than that of the operating environment. It is used quite often in designing electronic components.

## Slide 33: More Derating
Failure Rate of a gear:
 b = base failure rate specified by the manufacturer
s = operating speed
sd = design speed
L = operating load
Ld = design load
v = viscosity of lubricant used
vs = viscosity of specification lubricant
c = concentration of contaminants
cs =standard contamination level
T = operating temperature
Ts = specification temperature
Notes: Derating can also be applied to mechanical failure modes.

## Slide 34: Stress-Strength Analysis
Concerned when abnormal loads are possible
Probabilistic compare the magnitude of the stress with the design strength.
Use physical models
Major categories of stress
  electrical
  thermal
  mechanical
  chemical
Two design approaches
  select parts with sufficient strength against max load
  protect part against excessive stresses
Looking for strength to
cope with the stress!
Notes: Computing the reliability by comparing the stress probability distribution with the strength probability distribution as was done in Chapter 7 is part of the stress-strength analysis. If the reliability is insufficient, then either greater strength must be designed into the part or the part must be protected from abnormally high stresses levels.

## Slide 35: Stress - Strength Analysis
Safety Factor = Y/X
Notes: These curves are based upon lognormal stress and strength distributions. traditional engineering defines the safety factor as the (mean) strength divided by the (mean) stress. However, as these curve show, even for a safety factor of 5, there can be a ten percent chance or more of a failure occurring depending upon the shape parameters of the distributions.

## Slide 36: Stress Protection
Electronic Circuit Boards
Notes: Some methods for stress protection.

## Slide 37: Redundancy
Notes: Analyzing reliability under redundancy was discussed in Chapters 5 and 6. The design engineer has several forms of redundancy to select from. Typically redundancy will be used when exceptionally high reliability cannot be achieved using other techniques.

## Slide 38: Redundancy
Advantages
Quickest way to improve reliability
May be cheapest vs. cost of redesign
May be the only solution if specified reliability is beyond the state of the art
Disadvantages
Sensors and switching may increase cost and reduce reliability
May exceed size, weight or power constraints
Increases maintainability requirements
Notes: Redundancy is not without its disadvantages.

## Slide 39: Conclusion
As an engineer, I can assure you that these design methods work.